## Slide 1: Protecting the Safety and Health of Workers
Brian Bothast
Occupational Safety and Health Administration

## Slide 2: Topics
Inspections 101
National Emphasis Programs
Local Emphasis Programs
COVID-19
Questions

## Slide 3: OSHA Inspections
Fatality / Catastrophe
Complaint / Referral
Follow-up
Scheduled inspections
National Emphasis Program
Regional Emphasis Program
Severe Injury Report

## Slide 4
Employers must contact OSHA for:
All work-related fatalities within 8 hours
All work-related in-patient hospitalizations of one or more employees within 24 hours
All work-related amputations within 24 hours
All work-related losses of an eye within 24 hours
  1-800-321-OSHA (6742)

## Slide 5: The general duty clause. Section 5(a)(1)
Each employer shall furnish a place of employment free of recognizable hazards that are likely to cause serious physical harm.

## Slide 6: OSHA must prove
Exposed employee
Serious hazard
Employer knowledge
Feasible method to abate hazard

## Slide 7: Do you have a truly effective safety and health program?
Clear rules and expectations?
Employees understand the rules and expectations?
An effective process to discover deviations from expectations?
An effective enforcement program?

## Slide 8: National Emphasis Programs
Excavations
Hazardous Machinery
  (amputations)
Combustible Dust
Hexavalent Chromium
Lead
Silica
Primary Metal Industries
Shipbreaking
Process Safety Management
Coronavirus (COVID-19)

## Slide 9: NEP - excavations and cave-in hazards
Cave-in protection
Ladder
Spoil pile
Competent person inspections
Training

## Slide 10: Lead NEP
Air monitoring
Written compliance program
Personal protective equipment / Respirator program
Hygiene – Shower and storage
Medical program
Lead program training

## Slide 11: Hexavalent Chromium
Includes the following industries
  Welding stainless steel
  Electroplating, Plating, Polishing, Anodizing and Coloring Industry
  Gray and Ductile Iron Foundries
  Metal Fabrication Shops
  Scrap Metal Industry

## Slide 13: Local Emphasis Programs
Fall Hazards in Construction and General Industry
Powered Industrial Vehicles
Grain Handling Facilities
High Rise Building Construction Inspections
Building Renovation/Rehabilitation and Demolition
Wood Pallet Manufacturing Industry
Federal Agencies
Maritime Industries
Noise Hazards
Transportation Tank Cleaning Operation

## Slide 14: Powered industrial vehicles
Vehicle and worksite specific training
Evaluation
Daily checks
Failure to remove from service

## Slide 15: Building Renovation
initiated by CSHO observation, complaints and referrals from municipal inspectors, etc.
Targeted sites include extensive interior demolition and demolition of part of buildings.

## Slide 16: High Rise Building Construction Inspections in Chicago IL
The targeting and selection program is intended to be used on those new construction projects which are 10 stories tall or greater.
Focused Inspections
Compliance Officers shall collect OSHA 300 logs on all worksites where the general contractor maintains a log for the entire worksite.

## Slide 17: Transportation Tank Cleaning Emphasis program
484110 General Freight Trucking, Local
488210 Support Activities for Rail Transportation
488490 Other Support Activities for Road Transportation
488510 Freight Transportation Arrangement
562910 Remediation Services
562920 Materials Recovery Facilities
562998 All Other Miscellaneous Waste Management Services

## Slide 18: Inspection Procedures
Review
  Permit Required Confined Space Program
  Respiratory Protection Program
  Hearing conservation program
  Hazard Communication
  Personal Protective Equipment
  Others Hazards: chemicals, thermal, electrical, fall, and struck-by hazards

## Slide 19: Oxygen…
20.8%

## Slide 20: Carbon monoxide
an employee was unloading his semi-truck tanker of flour and hooked up a blower hose that is powered from the truck's transmission.

## Slide 21: Hydrogen sulfide
At 4:00 p.m. on May 24, 2019, a farmer entered a 1,500 gallon bulk milk tank to clean it with well water. The employee died due to the inhalation of hydrogen sulfide from the well water. The lack of ventilation in the tank trapped the gas.

## Slide 22: Chemicals
On July 29, 2019, two employees were preparing to start seeding a high school football field using a hydro seeding truck. Employee #1 was overcome by the fumes within the tank. Employee #2 went to help. Employee #2 was overcome from the vapors within the tank and both employees were asphyxiated.

## Slide 23: hazard communication program
Management responsibility for program
Develop list of hazardous chemicals
Label hazardous chemical containers
Manage Safety Data Sheets
Procedures for training exposed employees
Address the hazards of non-routine tasks
Procedures for Multi-employer workplaces

## Slide 24: Heat illness prevention
Workers gradually build up to heavy work (acclimated)
Know signs of heat illnesses
Water intake plan
Management check of workers
Plan for emergencies
Notes: Overview
Workers who are exposed to extreme heat or work in hot environments may be at risk of heat stress. Exposure to extreme heat can result in occupational illnesses and injuries. Heat stress can result in heat stroke, heat exhaustion, heat cramps, or heat rashes. Heat can also increase the risk of injuries in workers as it may result in sweaty palms, fogged-up safety glasses, and dizziness. Burns may also occur as a result of accidental contact with hot surfaces or steam.
Workers at risk of heat stress include outdoor workers and workers in hot environments such as firefighters, bakery workers, farmers, construction workers, miners, boiler room workers, factory workers, and others. Workers at greater risk of heat stress include those who are 65 years of age or older, are overweight, have heart disease or high blood pressure, or take medications that may be affected by extreme heat.
Prevention of heat stress in workers is important. Employers should provide training to workers so they understand what heat stress is, how it affects their health and safety, and how it can be prevented.
Types of Heat Stress
Heat Stroke | Heat Exhaustion | Heat Syncope | Heat Cramps | Heat Rash
Heat Stroke
Heat stroke is the most serious heat-related disorder. It occurs when the body becomes unable to control its temperature: the body's temperature rises rapidly, the sweating mechanism fails, and the body is unable to cool down. When heat stroke occurs, the body temperature can rise to 106 degrees Fahrenheit or higher within 10 to 15 minutes. Heat stroke can cause death or permanent disability if emergency treatment is not given.
Symptoms
Symptoms of heat stroke include:
Hot, dry skin (no sweating)
Hallucinations
Chills
Throbbing headache
High body temperature
Confusion/dizziness
Slurred speech
First Aid
Take the following steps to treat a worker with heat stroke:
Call 911 and notify their supervisor.
Move the sick worker to a cool shaded area.
Cool the worker using methods such as:
  Soaking their clothes with water.
  Spraying, sponging, or showering them with water.
  Fanning their body.
Heat Exhaustion
Heat exhaustion is the body's response to an excessive loss of the water and salt, usually through excessive sweating. Workers most prone to heat exhaustion are those that are elderly, have high blood pressure, and those working in a hot environment.
Symptoms
Symptoms of heat exhaustion include:
Heavy sweating
Extreme weakness or fatigue
Dizziness, confusion
Nausea
Clammy, moist skin
Pale or flushed complexion
Muscle cramps
Slightly elevated body temperature
Fast and shallow breathing
First Aid
Treat a worker suffering from heat exhaustion with the following:
Have them rest in a cool, shaded or air-conditioned area.
Have them drink plenty of water or other cool, nonalcoholic beverages.
Have them take a cool shower, bath, or sponge bath.
Heat Syncope
Heat syncope is a fainting (syncope) episode or dizziness that usually occurs with prolonged standing or sudden rising from a sitting or lying position. Factors that may contribute to heat syncope include dehydration and lack of acclimatization.
Symptoms
Symptoms of heat syncope include:
Light-headedness
Dizziness
Fainting
First Aid
Workers with heat syncope should:
Sit or lie down in a cool place when they begin to feel symptoms.
Slowly drink water, clear juice, or a sports beverage.
Heat Cramps
Heat cramps usually affect workers who sweat a lot during strenuous activity. This sweating depletes the body's salt and moisture levels. Low salt levels in muscles causes painful cramps. Heat cramps may also be a symptom of heat exhaustion.
Symptoms
Muscle pain or spasms usually in the abdomen, arms, or legs.
First Aid
Workers with heat cramps should:
Stop all activity, and sit in a cool place.
Drink clear juice or a sports beverage.
Do not return to strenuous work for a few hours after the cramps subside because further exertion may lead to heat exhaustion or heat stroke.
Seek medical attention if any of the following apply:
  The worker has heart problems.
  The worker is on a low-sodium diet.
  The cramps do not subside within one hour.
Heat Rash
Heat rash is a skin irritation caused by excessive sweating during hot, humid weather.
Symptoms
Symptoms of heat rash include:
Heat rash looks like a red cluster of pimples or small blisters.
It is more likely to occur on the neck and upper chest, in the groin, under the breasts, and in elbow creases.
First Aid
Workers experiencing heat rash should:
Try to work in a cooler, less humid environment when possible.
Keep the affected area dry.
Dusting powder may be used to increase comfort.
Recommendations for Employers
Employers should take the following steps to protect workers from heat stress:
Schedule maintenance and repair jobs in hot areas for cooler months.
Schedule hot jobs for the cooler part of the day.
Acclimatize workers by exposing them for progressively longer periods to hot work environments.
Reduce the physical demands of workers.
Use relief workers or assign extra workers for physically demanding jobs.
Provide cool water or liquids to workers.
  Avoid drinks with caffeine, alcohol, or large amounts of sugar.
Provide rest periods with water breaks.
Provide cool areas for use during break periods.
Monitor workers who are at risk of heat stress.
Provide heat stress training that includes information about:
  Worker risk
  Prevention
  Symptoms
  The importance of monitoring yourself and coworkers for symptoms
  Treatment
  Personal protective equipment
Recommendations for Workers
Workers should avoid exposure to extreme heat, sun exposure, and high humidity when possible. When these exposures cannot be avoided, workers should take the following steps to prevent heat stress:
Wear light-colored, loose-fitting, breathable clothing such as cotton.
  Avoid non-breathing synthetic clothing.
Gradually build up to heavy work.
Schedule heavy work during the coolest parts of day.
Take more breaks in extreme heat and humidity.
  Take breaks in the shade or a cool area when possible.
Drink water frequently. Drink enough water that you never become thirsty.
Avoid drinks with caffeine, alcohol, and large amounts of sugar.
Be aware that protective clothing or personal protective equipment may increase the risk of heat stress.
Monitor your physical condition and that of your coworkers.
CDC Resources
MMWR: Heat-Related Deaths among Crop Workers, 1992-2006
CDC: Extreme Heat Additional information on heat stress illnesses and prevention. En Español
NIOSH: Criteria for a Recommended Standard: Occupational Exposure to Hot Environments (Revised Criteria 1986) This document presents the criteria, techniques, and procedures for the assessment, evaluation, and control of occupational heat stress by engineering and preventive work practices. Included are ways of predicting health risks, procedures for control of heat stress, and techniques for prevention and treatment of heat-related illnesses.
NIOSH: Working in Hot Environments Workers who are suddenly exposed to working in a hot environment face additional and generally avoidable hazards to their safety and health. This publication discusses the safety and health consequences of heat stress.
Health Hazard Evaluations
Health Hazard Evaluation Report, HETA 2004-0334-3017, Transportation Security Administration, Palm Beach International Airport, West Palm Beach, Florida
Health Hazard Evaluation Report, HETA 2003-0311-3052 , Evaluation of Heat Stress at a Glass Bottle Manufacturer, Lapel, Indiana
Health Hazard Evaluation Report, HETA 2000-0061-2885, United States Air Force, Seymour Johnson air Force Base, Goldsboro, North Carolina
Other Government Resources
Occupational Safety and Health Administration (OSHA) Safety and Health Topics: Heat Stress Provides a guide to information regarding the recognition, evaluation, control, and compliance actions involving heat stress.
OSHA Technical Manual Section III: Chapter 4 - Heat Stress Provides descriptions of heat disorders, investigative guidelines, sampling methods, control, and PPE.
OSHA Sawmills eTool: Heat Stresses Provides information on the hazards of heat stress and possible solutions or controls.
OSHA Quick Card: Heat Stress Provides heat stress factors, symptoms, prevention tips, and first aid recommendations. En Español
OSHA Fact Sheet: Protecting Workers from Effects of Heat [PDF - 22 KB] Provides information that will help workers understand what heat stress is, how it may affect their health and safety, and how it can be prevented.
OSHA Fact Sheet: Working Outdoors in Warm Climates [PDF - 25 KB] Hot summer months pose special hazards for outdoor workers who must protect themselves against heat, sun exposure, and other hazards. Employers and employees should know the potential hazards in their workplaces and how to manage them.

## Slide 25: Respiratory Protection Program
Program Administrator
Written program – selection process
  Do you know the level of the contaminant?
Medical evaluation
Fit test
Training
Recordkeeping

## Slide 26: National Emphasis Program Coronavirus Disease 2019
OSHA 300 and 300A
Exposure incidents, employees who contracted COVID-19, have been hospitalized or isolated as a result of exposure to SARS-CoV-2.
Written COVID-19 plan
Evidence of hazard assessment.
Controls - physical distancing, barriers, etc.
Respiratory protection program for COVID-19
Personal Protective Equipment
Training related to SARS-CoV-2 prevention.
Engineering controls such as HVAC systems

## Slide 27: For continual updates
Visit OSHA’s website for information:
  www.osha.gov
  QuickTakes biweekly newsletter
Follow OSHA on social media
  Twitter: @OSHA_DOL

## Slide 28
Brian Bothast
bothast.brian@dol.gov
309-589-7125
Questions?